## Slide 1: Intel E2E Setup

## Slide 2: Intel E2E Topology
G.M
5gc Switch
Remote Control
RJ45
L1+DU+CU
10G/SFP+
10G/SFP+
RJ45
enp61s0f0
FIber enp61s0f1
USB3.1
USB
USB
Example ASRock 11
Fiber
5GC
Dell Switch
1
2
3
4
Foxconn need
WNC (X)

## Slide 3: Intel E2E Topology
5gc Switch
Remote Control
L1+DU+CU
10G/SFP+
10G/SFP+(vlan 1111)
enp61s0f0(vlan 1111)
enp134s0f1
USB3.1
Example ASRock 12
Fiber
5GC
Dell Switch
1
2
3
4

## Slide 4: Prepare for GNB server
Asrock#11
Intel Mount Bryce
a
b
Example:
Port a: Connnect to DELL switch setup for serving RU connect / IEEE 1588 TimeSync
Port b: Connnect to 5gc switch setup for serving affirmed 5gc
Port c: QAT for CU using HW CRYPTO
Intel Mount Bryce for Flexran init
c
Before setup you need to prepare
1. Intel E10GSFPSR or 25G at least x4
2. Fiber Cable at least x2
3. QAT Card (check server) x1
4. Mount Bryce (check server) x1
You could register and brrow these item with Tina
!請確定各光孔的連接目的

## Slide 5: Checking for Asrock PCI bus device
Checking for Asrock PCI bus device
[root@5gran-asrock-11 docker-gnb]#
lspci
Port a: Connnect to DELL switch setup for serving RU connect
/ IEEE 1588 TimeSync
Port b: Connnect to 5gc switch setup for serving free5gc
Port c: QAT for CU using HW CRYPTO
Intel Mount Bryce for Flexran init
Asrock
Intel Mount Bryce
a
b
c

## Slide 6: Checking for Asrock PCI Device Driver
Checking for Asrock PCI Device Driver
[root@5gran-asrock-11 docker-gnb]#
dpdk-devbind -s
Asrock
Intel Mount Bryce
a
b
c

## Slide 7: GNB Env Setup
for example
#enp61s0f0 #Port a
echo 0 > /sys/bus/pci/devices/0000\:3d\:00.0/sriov_numvfs
echo 8 > /sys/bus/pci/devices/0000\:3d\:00.0/sriov_numvfs
ip link set dev enp61s0f0 vf 0 mac 00:11:34:86:0a:00 state enable vlan 1111
ip link set dev enp61s0f0 vf 1 mac 00:11:34:86:0a:01 state enable vlan 1111
ip link set dev enp61s0f0 vf 2 mac 00:11:33:3d:02:03 state enable
ip link set dev enp61s0f0 vf 3 mac 00:11:33:3d:02:04 state enable
ip link set dev enp61s0f0 vf 4 mac 00:11:33:3d:02:05 state enable
ip link set dev enp61s0f0 vf 5 mac 00:11:33:3d:02:06 state enable
#enp61s0f1 #Port b
echo 0 > /sys/bus/pci/devices/0000\:3d\:00.1/sriov_numvfs
echo 8 > /sys/bus/pci/devices/0000\:3d\:00.1/sriov_numvfs
ip link set dev enp61s0f1 vf 0 mac 00:11:99:3d:0e:0 state enable
ip link set dev enp61s0f1 vf 1 mac 00:11:99:3d:0e:1 state enable
ip link set dev enp61s0f1 vf 2 mac 00:11:99:3d:0e:2 state enable
ip link set dev enp61s0f1 vf 3 mac 00:11:99:3d:0e:3 state enable
ip link set dev enp61s0f1 vf 4 mac 00:11:99:3d:0e:4 state enable
ip link set dev enp61s0f1 vf 5 mac 00:11:99:3d:0e:5 state enable
Asrock
Intel Mount Bryce
a
b
c
Should following gnbctl to setup
./gnbctl profile set radisys251_affirmed5gc ./gnbctl sriov init
./gnbctl cu init
./gnbctl du init
./gnbctl flexran init
!光孔不同目的配合不同設置
連接 RU的MAC 需與WNC寫入的MAC相符

## Slide 8: dpdk-devbind and ifconfig
For Example
Asrock
Intel Mount Bryce
a
b
c
#3d port1 #RU
dpdk-devbind -b vfio-pci 3d:02.{0,1}
dpdk-devbind -b iavf 3d:02.{2,3,4,5}
#3d port2 #5gc
dpdk-devbind -b iavf 3d:0a.{0,1}
dpdk-devbind -b igb_uio 3d:0a.{2,3,4,5}
#MountBryceCard using on docker-flexran5g.env
dpdk-devbind -b vfio-pci 5f:00.2
ifconfig enp61s2f3 192.168.50.133 netmask 255.255.255.0 up
ifconfig enp61s2f5 192.168.50.135 netmask 255.255.255.0 up
ifconfig enp61s10f1 192.168.120.92 netmask 255.255.255.0 up
ifconfig enp61s2f2 4.4.4.33 netmask 255.255.255.0 up
ifconfig enp61s2f4 4.4.4.35 netmask 255.255.255.0 up
ifconfig enp61s10 5.5.5.92 netmask 255.255.255.0 up
Match with docker-gnb.env and CU/DU oam_config

## Slide 9
UE
Docker GNB_0.1.0.7 Topology #Asrock11
M5
gNB DU
gNB CU
DU_F1U
CU_F1U
enp61s6f1
4.4.4.103
DU_F1C
CU_F1C
192.168.10.102
192.168.10.103
CU_NGU
CU_NGC
NGU 172.16.20.14
NGC
172.16.17.226
172.16.30.1 172.16.29.1
172.16.30.118
172.16.29.118
SCTP
RU0
enp61s6f2
enp134s2f1
enp134s2f2
enp134s10f1
enp134s10f2
enp61s0f0
4.4.4.102
MiFi
RU0_FHU/FHC
gNB Flexran
Affirmed
iperf3
172.16.26.123
172.16.26.125

## Slide 10
UE
Docker GNB_0.1.0.7 Topology #Asrock12
M5
gNB DU
gNB CU
DU_F1U
CU_F1U
enp61s6f1
4.4.4.17
DU_F1C
CU_F1C
192.168.10.65
192.168.10.17
CU_NGU
CU_NGC
NGU 172.16.20.14
NGC
172.16.17.226
172.16.30.1 172.16.29.1
172.16.30.110
172.16.29.110
SCTP
RU0
enp61s6f2
enp134s2f1
enp134s2f2
enp134s10f1
enp134s10f2
enp61s0f0
4.4.4.65
MiFi
RU0_FHU/FHC
gNB Flexran
Affirmed
iperf3
172.16.26.123
172.16.26.125

## Slide 11
UE
Docker GNB_0.0.7 Topology #Asrock11
M5
gNB DU
gNB CU
DU_F1U
CU_F1U
enp61s2f2
4.4.4.5
DU_F1C
CU_F1C
192.168.50.100
192.168.50.105
CU_NGU
CU_NGC
AMF:N2 192.168.120.101
SMF:N4 192.168.104.33
UPF:N6 192.168.105.132
5.5.5.72
192.168.120.72
5.5.5.101
VS
192.168.105.201
GTP-U / N3
SCTP
RU0
enp61s2f3
enp61s2f4
enp61s2f5
enp61s10
enp61s10f1
enp61s0f0
4.4.4.3
MiFi
RU0_FHU/FHC
gNB Flexran
free5gc
iperf3

## Slide 12
UE
Docker GNB_0.1.0 Topology #Asrock12
M5
gNB DU
gNB CU
DU_F1U
CU_F1U
enp61s10f2
4.4.4.17
DU_F1C
CU_F1C
192.168.10.65
192.168.10.107
CU_NGU
CU_NGC
AMF:N2 192.168.120.202
SMF:N4 192.168.104.134
5.5.5.107
VS
SCTP
RU0
enp61s10f3
enp134s2f1
enp134s2f2
enp61s14
enp61s14f1
enp61s0f0
4.4.4.65
MiFi
RU0_FHU/FHC
gNB Flexran
free5gc
iperf3
192.168.105.201
UPF:N6 192.168.105.233
5.5.5.203
CU_NGU
CU_NGC
192.168.120.107
enp134s10f1
172.16.30.107
enp134s10f2
172.16.29.107
NGU
172.16.20.14
NGC
172.16.17.226
172.16.29.1 172.16.30.1
IPERF3
172.16.26.123
Affirmed

## Slide 13: RU Init & O-du test
Asrock #12
RU Init (Foxconn)
  Power on RU, check console status
  ./set_port.sh 0
  ./init_rrh_config_enable_cuplane (wait for 10 min)
O-du test check
cd /home ; ./odu_test.sh
GNB PTP Check
cd /home ; ./do_ptp.sh

## Slide 14: RU Init
Asrock #12
RU Init (WNC)
  show ptp clock(wait the ptp lock)
  radio enable
RU vlan setting
GNB PTP Check
tail -f /var/log/message

## Slide 15: WNC RU INIT setting
RU Init (WNC)
#n78 power command
fpga write 0xff220008 0x08000001
radio debug radioctrlcfg-set 0 0 0xf
radio debug radioctrlcfg-set 1 0 0xf
radio debug pa-set 0x0
radio debug paprot 2200
radio debug pa-set 0x1
radio debug rxtx-en 0x1 0x0
radio debug pa-set 0x0
radio debug rxtx-en 0x0 0x0
radio debug radioctrlcfg-set 0 1 0x1
radio debug radioctrlcfg-set 0 1 0x2
radio debug radioctrlcfg-set 0 1 0x4
radio debug radioctrlcfg-set 0 1 0x8
radio debug radioctrlcfg-set 1 1 0x1
radio debug radioctrlcfg-set 1 1 0x2
radio debug radioctrlcfg-set 1 1 0x4
radio debug radioctrlcfg-set 1 1 0x8
fpga write 0xff220008 0x0
radio debug lna-set 0 0xf
#n79 power command
fpga write 0xff220008 0x08000001
radio debug radioctrlcfg-set 0 0 0xf
radio debug radioctrlcfg-set 1 0 0xf
radio debug pa-set 0x0
radio debug paprot 1900
radio debug pa-set 0x1
radio debug rxtx-en 0x1 0x0
radio debug pa-set 0x0
radio debug rxtx-en 0x0 0x0
radio debug radioctrlcfg-set 0 1 0x1
radio debug radioctrlcfg-set 0 1 0x2
radio debug radioctrlcfg-set 0 1 0x4
radio debug radioctrlcfg-set 0 1 0x8
radio debug radioctrlcfg-set 1 1 0x1
radio debug radioctrlcfg-set 1 1 0x2
radio debug radioctrlcfg-set 1 1 0x4
radio debug radioctrlcfg-set 1 1 0x8
fpga write 0xff220008 0x0
radio debug lna-set 0 0xf
Login id/pwd : root/(null)
enable
# setup mac of RU
config interface eth1
shutdown
mac-address 00:aa:ff:bb:aa:34
no shutdown
exit
exit
# setup mac of DU 00:11:34:86:0a:00
fpga write 0xff25008c 0x34860a00
fpga write 0xff250090 0x00000011
radio enable

## Slide 16: Free5gc Init
ssh pega@10.255.174.18 (password: pega#1234)
cd free5gc.cell2/
docker-compose ps
docker-compose down
docker-compose up -d
./show-log.sh
UPF Restart
dokcker-compose down
./imec-upf-restart.sh
docker-co mpose up

## Slide 17: UE Control (at command)
ATE0 (not display)
ATE1 (display)
ATI (Product Identification)
AT+CFUN=0 (Minimum function)
AT+CFUN=1 (Full function)
### check sim status ###
AT+CPIN?
### GET IMSI ### AT+CIMI
### GET IMEI ### AT+GSN
### GET CESQ ### AT+CESQ
### Search Network Operation###
at_cmd.sh at+cops=?
### Network registration status###
at_cmd.sh at+cops?
at_cmd.sh at+cops=1,2,”00101”
### Check APN/DNN Setting###
at_cmd.sh at+cgdcont?
### Set APN/DNN Setting###
at_cmd.sh at+cgdcont=1,”IP”,”PEGAPN-LD3”

## Slide 18: Initial power tuning tool - by Fangming
Theoretical value through open loop power control turning tool:

## Slide 19: Bring-up sanity test - QXDM logging check
Item | Key | QXDM filter
Registration procedure (RRC/NAS) | - | Log Packets(OTA)/NR5G/NAS Log Packets(OTA)/NR5G/RRC
L1, L2 Analyze | 0076/04 | QTraces/COMMON/QSH/ANALYSIS
MAC layer information (ex. RACH, DCI info, PDSCH status, ...) | - | Log Packets/NR5G/MAC
TX Power | 0XB8D2 | Log Packets/LL1/FW/NR5G LL1 FW MAC TX IU power
RSSI | 0xB8C9 | Log Packets/LL1/FW/NR5G LL1 FW RX Control AGC
RSRP/RSRQ | 0xB97F | Log Packets/ML1/NR5G ML1 Searcher Measurement Database Update Ext
SINR | 0042/00 | QTraces/MMCP/MMODE/

## Slide 20: AsRock#11 init
Run PTP
  cd /home/wnc
  ./do_ptp.sh
  tail -f /var/log/message
掛載vfio-pci
  sudo modprobe vfio-pci
docker init
  cd /home/wnc/docker-gnb_0.1.0.7/docker-gnb
  ./gnbctl sriov init
  ./gnbctl flexran init
  ./gnbctl du init
  ./gnbctl cu init
Check the NG connect
  ping 172.16.29.1; 172.16.30.1; 172.16.20.1; 172.16.17.1

## Slide 21: AsRock#12 init
Run PTP
  cd /data2
  ./setup_ota_e2e ptp_old
  tail -f /var/log/message ; tail -f /var/log/phc2sys
docker init
  cd /data2/wnc/docker-gnb_0.1.0/docker-gnb
  ./gnbctl sriov init
  ./gnbctl flexran init
  ./gnbctl du init
  ./gnbctl cu init
Check the NG connect
  ping 172.16.29.1; 172.16.30.1; 172.16.20.1; 172.16.17.1

## Slide 22: Docker 0.1.0.7 env setup
Git docker-gnb project
  git clone ssh://git@172.18.220.81:10022/5g-o-ran/gnodeb/docker-gnb.git
設定profile
  cd docker-gnb/
  ./gnbctl profile clear
  ./gnbctl profile set radisys251_affirmed5gc
PCI、QAT、MCC、MNC設定(docker-gnb.env)
  cd profile/active/
  vim docker-gnb.env
設定NGU/NGC
設定QAT PCI

## Slide 23: Docker 0.1.0.7 env setup
DU Setting(CPU、ip)
CU Setting(QAT、network card、vlan)
F1C/F1U ip setting
CU F1C/F1U ip setting
CU NgC/NgU ip setting

## Slide 24: Docker 0.1.0.7 env setup
RU 、 DU MAC 、 vlan setting(docker-flexran.env)
DU and RU mac setting

## Slide 25: Iperf 指令
iperf server(172.16.26.123)
  位置在Demo room地上主機
  cd /home/pega
  ./kill_iperf3_servers_FM.sh
  ./iperf3_BG_FM.sh
iperf server(172.16.26.125)
  ssh pega@10.255.174.121(passoword: Pega#1234)
  iperf3 -s -p 40000(40000~49999皆可使用)
iperf throughput
  iperf3 -c (.123 or .125) -p (40000~49999) -t (時間) -w (window size) -l (len) -u(有為UDP,沒有為TCP) -b (頻寬) -R(有為downlink,沒有為uplink)
  example: iperf3 -c 172.16.26.125 -p 40000 -t 120 -w 410K -l 1300 -u -b 600m -R

## Slide 26: Docker container Problem
解決方式:
1. 檢查, docker-compose ps -a
2. 將目前執行之docker container 停掉, docker-compose down
3. 檢查, docker network ls
4. docker network rm NETWORK_ID
5. sudo systemctl restart docker